## Slide 1: CS 685 Autonomous Robotics Motion Planning IV
Prof. Xuesu Xiao
George Mason University
Slides Credits: Gregory Stein

## Slide 2: Vehicle Dynamics & Motion Primitives

## Slide 3: We talked about how to build C-space. How do we plan with it?

## Slide 4: We talked about how to build C-space. How do we plan with it?
There were a number of approaches we talked about that will still work here!
Discretization (into a grid)
Voronoi decomposition (not great in high-dimensions)
Visibility graph planning (also not great in High-D)

## Slide 5: We talked about how to build C-space. How do we plan with it?
We’ve been so focused on building configuration space that we haven’t really defined how planning will work yet…
We could discretize the space, but that’s non-ideal for a few reasons: what were the problems with discretizing continuous space (e.g., grid-based planning)?

## Slide 6: Remember this?
But turning a continuous space into a grid, you must trade off between a very small resolution (and high computational cost) or a big resolution (and miss closing off paths):
This approach is therefore not complete in general!
Image from: MIT 16.410

## Slide 7: What were the problems with discretizing continuous space (e.g., grid-based planning)?
Not complete in general
Can be expensive if we make the grid cells very small to handle tight passages. Also expensive in high dimensions.

## Slide 8: What were the problems with discretizing continuous space (e.g., grid-based planning)?
Not complete in general
Can be expensive if we make the grid cells very small to handle tight passages. Also expensive in high dimensions.
Also: what about vehicle dynamics (again)?
You can’t simply move along the x-direction.
The car is limited in how it can move through C-space.

## Slide 9: Recap: There are some limitations of our planning abstractions or representations thus far
If I’m a self-driving car, can I follow this path?
No! Why not?
Size: The vehicle cannot get infinitesimally close to objects.
Dynamics: The vehicle has a finite turning radius.

## Slide 10: Recap: There are some limitations of our planning abstractions or representations thus far
If I’m a self-driving car, can I follow this path?
No! Why not?
Size: The vehicle cannot get infinitesimally close to objects.
Dynamics: The vehicle has a finite turning radius.

## Slide 11: Recap: There are some limitations of our planning abstractions or representations thus far
If I’m a self-driving car, can I follow this path?
No! Why not?
Size: The vehicle cannot get infinitesimally close to objects.
Dynamics: The vehicle has a finite turning radius.
Planning Time: I might have a hard time planning in a reasonable amount of time

## Slide 12: We have established that there are advantages of planning in continuous space
We can recover the optimal action, something that’s not possible when planning in discrete space.
However, planning in continuous space is incredibly difficult because we have an infinite number of possible trajectories…

## Slide 13: Different planning modalities
Grid-based planning
  discrete states, discrete actions
“Continuous-space Planning” (we still haven’t really defined this)
  continuous states, continuous actions
Hypothesis: What if instead the robot could take discrete actions, but these actions still happened in continuous space?

## Slide 14: Motion Primitives: discrete actions that happen in continuous space
Let’s pretend that the actions available to the robot are discrete.

## Slide 15: Where do motion primitives come from?
It very much depends on the scenario.
Some robots are pretty simple: e.g., a point robot that can move in every direction. Basically what we’ve been doing already.
Some are more complicated: e.g., a Dubins Car, a car, or a “snake-like robot” with multiple links.

## Slide 16: Where do motion primitives come from?
Dubins Car: a car that can go forward, turn “all the way left” or ”all the way right” with some fixed turning radius.

## Slide 17: Where do motion primitives come from?
Dubins Car: a car that can go forward, turn “all the way left” or ”all the way right” with some fixed turning radius.
”Dubins curves are also the fastest trajectories for a simple model of a steered car that moves with unit velocity.”
From: https://rlab.cs.dartmouth.edu/publications/Furtuna2010.pdf

## Slide 18: Where do motion primitives come from?
Reeds-Shepp Car: a Dubins car that can also go backwards.
From: https://rlab.cs.dartmouth.edu/publications/Furtuna2010.pdf

## Slide 19: Other models may consider how max turning radius changes with speed.

## Slide 20: Motion Primitives: discrete actions that happen in continuous space
Let’s pretend that the actions available to the robot are discrete. What can we do with these?

## Slide 21: Monte-Carlo Methods

## Slide 22: Let’s say you wanted to compute the area of a circle…
But you can’t use calculus or equations you know?
How might you do this?

## Slide 23: Let’s say you wanted to compute the area of a circle…
But you can’t use calculus or equations you know?
How might you do this?
Polygonal approximation? Try to bound the area by drawing regular polygons inside and outside the circle?
Geometry? Draw some triangles over the surface

## Slide 24: Let’s say you wanted to compute the area of a circle…
What if you printed out the shape and threw a dart at it?
If you aim is totally random, what’s the probability you’re inside the square, but not the circle?
Image Credit

## Slide 25: Let’s say you wanted to compute the area of a circle…
What if you printed out the shape and threw a dart at it?
If you aim is totally random, what’s the probability you’re inside the square, but not the circle?
Image Credit
P = 1 - Acircle / Asquare

## Slide 26: Monte Carlo Sampling: throwing darts
Idea: we throw a lot of darts and the number that are inside the circle will tell us what its area is.

## Slide 27: Monte Carlo Sampling: throwing darts
Idea: we throw a lot of darts and the number that are inside the circle will tell us what it’s area is.
As we get more samples, our approximation gets better.
In many cases, this can be way faster than trying to get an exact solution.
Image: Wikipedia

## Slide 28: So-called “Monte Carlo Methods” or “Random Sampling” will come up again
It’s a very useful technique: often fast to get a “good enough” solution for a lot of problems where the “exact” solution is expensive and hard to derive.
Applications:
Numerical integration (very useful in high dimensions)
Sampling from probability distributions (Markov Chain Monte Carlo [MCMC] methods)
Game-playing (will come up again later on)
Motion Planning (today)

## Slide 29: Sampling-Based Motion Planning
With multiple slides from P. Abbeel’s CS287 (Berkeley), papers, and S. LaValle’s textbook.

## Slide 30: So if we don’t want to do search how are we going to plan (using randomness)?
Simply expanding the set of motion primitives was pretty inefficient.
For now, let’s ignore vehicle dynamics: they’ll come back later, but it will be helpful for the time being if we don’t have to “worry” about them.
We also still have full knowledge of the state of the world. This means we can easily tell when the vehicle collides with obstacles in the world.

## Slide 31: Planning with random sampling
In MC sampling, we used randomness to our advantage to avoid needing to solve the problem exactly and exhaustively.
What are our options?
We could try just picking some random actions, but that’s not particularly intelligent.

## Slide 32: Planning with random sampling
In MC sampling, we used randomness to our advantage to avoid needing to solve the problem exactly and exhaustively.
What are our options?
We could try just picking some random actions, but that’s not particularly intelligent.
What about using randomness to build a roadmap?

## Slide 33: The Probabilistic Roadmap (PRM)
Let’s try that: use randomness to build a roadmap.
General procedure:
Pick a bunch of random points (e.g., uniformly across your domain)
Add visibility connections between those points: if we can travel directly between two of these, add an edge
The points and edges make up a roadmap, which we can then use for planning

## Slide 34: The Probabilistic Roadmap (PRM)

## Slide 35: The Probabilistic Roadmap (PRM)

## Slide 36: The Probabilistic Roadmap (PRM)

## Slide 37: The Probabilistic Roadmap (PRM)

## Slide 38: The Probabilistic Roadmap (PRM)

## Slide 39: The Probabilistic Roadmap (PRM)

## Slide 40: The Probabilistic Roadmap (PRM)

## Slide 41: The Probabilistic Roadmap (PRM)

## Slide 42: The Probabilistic Roadmap (PRM)

## Slide 43: The Probabilistic Roadmap (PRM)

## Slide 44: Conceptual Question: is PRM…
Complete?
Optimal?

## Slide 45: Conceptual Question: is PRM…
Complete?
Optimal?
It’s somewhat complicated: if we only have a finite number of points, it’s neither complete nor optimal.
What about if we had infinite points?

## Slide 46: Conceptual Question: is PRM…
Complete?
Optimal?
It’s somewhat complicated: if we only have a finite number of points, it’s neither complete nor optimal.
What about if we had infinite points? We say that PRM is asymptotically optimal: as we approach infinite samples, the algorithm becomes complete and optimal.

## Slide 47: Limitations of the PRM: What if we were to add back dynamics? What about computation?

## Slide 48: Plain PRM isn’t always a great choice, since you have to know too much in advance
The computation of the PRM happens in advance: we first pick all the points and compute the graph.
What if we don’t find a path between the start and goal?

## Slide 49: Plain PRM isn’t always a great choice, since you have to know too much in advance
The computation of the PRM happens in advance: we first pick all the points and compute the graph.
What if we don’t find a path between the start and goal? How about incremental PRM.
From: Kris Hauser’s Robotic Systems textbook

## Slide 50: Also, there’s lots to consider when sampling!
How do we decide where to sample points? Uniform sampling may be pretty inefficient. Some places need more samples than others; how do we pick these?
Narrow passages are notoriously hard.

## Slide 51: Also, there’s lots to consider when sampling!
Critically: many of the points we sample may not be useful to us.
They could be only connected in a small group and perhaps the robot can’t reach them (or will quickly realize that it doesn’t need to care about a region that’s very far away).

## Slide 52: Also, there’s lots to consider when sampling!
Critically: many of the points we sample may not be useful to us.
They could be only connected in a small group and perhaps the robot can’t reach them (or will quickly realize that it doesn’t need to care about a region that’s very far away).
Instead, we can use Rapidly exploring Random Trees another foundational approach that addresses some of these issues.

## Slide 53: Random Trees Building a tree out from a start point
Rather than building an entire graph (as in the PRM), we can build a tree instead.
Why? Think about search: we built a tree and expanded it when we needed to in an effort to reach the goal.
Idea: we start from the start point and randomly add new actions to that tree. But wait, I thought we already agreed that wasn’t a great idea…

## Slide 54: Random Trees Building a tree out from a start point
Naïve approach:

## Slide 55: Random Trees Building a tree out from a start point
Rather than building an entire graph (as in the PRM), we can build a tree instead.
Why? Think about search: we built a tree and expanded it when we needed to in an effort to reach the goal.
Idea: we start from the start point and randomly add new actions to that tree in some clever way that avoids adding a ton of nodes we don’t need.
So what is this cleverness?

## Slide 56: Rapidly exploring Random Trees (RRT) Building a tree out from a start point
Idea:
We have a tree and want to add a new branch to the tree.
We pick a random point we’d like to navigate towards.
We find the point in the tree that’s closest to that point already and move “1 unit” towards that point.

## Slide 57: Rapidly exploring Random Trees (RRT) Building a tree out from a start point
Idea:
We have a tree and want to add a new branch to the tree.
We pick a random point we’d like to navigate towards.
We find the point in the tree that’s closest to that point already and move “1 unit” towards that point. [Computed via the “EXTEND” function (also, more recently, known as the “steer” function)]

## Slide 58: What is the significance of “EXTEND/steer”?
First, we don’t want to get too far away with a single jump. Having a finite step size means we more slowly build the tree out from the center, rather than having edges jumping across the map, which can be difficult to deal with.
Second, it naturally supports the idea of having vehicle dynamics: we simply compute the control input that best moves the vehicle in the direction of our randomly sampled point. That means that every branch of the tree is automatically dynamically feasible!

## Slide 59: Rapidly exploring Random Trees (RRT) Algorithm
Together, these lines “steer towards” the random point from the nearest neighbor point.

## Slide 60: RRT Visualization [filling all the space]

## Slide 61: Multi-Directional RRT: build multiple RRTs simultaneously & connect to save cost

## Slide 62: RRT Properties
Is it complete?

## Slide 63: RRT Properties
Is it complete? Yes!

## Slide 64: RRT Properties
Is it complete? Yes!
Is it optimal?

## Slide 65: RRT Properties
Is it complete? Yes!
Is it optimal? No

## Slide 66: RRT is provably not asymptotically optimal
So what happened…?
Whenever we add new points, we extend old branches but we never look for new ways to reach the same point that might have been shorter!
Think of when we tried to add a visited list to A*, if we add points too early, we risk missing out on shorter paths.

## Slide 67: RRT is provably not asymptotically optimal
So what happened…?
Whenever we add new points, we extend old branches but we never look for new ways to reach the same point that might have been shorter!
Think of when we tried to add a visited list to A*, if we add points too early, we risk missing out on shorter paths.
This gap will never be closed

## Slide 68: How do we “fix” RRT
We need some way of looking for shortcuts.
Whenever we add new points, we should check if that new point allows us to reach other points sooner.

## Slide 69: How do we “fix” RRT
We need some way of looking for shortcuts.
Whenever we add new points, we should check if that new point allows us to reach other points sooner.
We add a new point: look at each nearby point. If the route through the new point to the nearby point is shorter than the old path, change the “root” of the nearby point to the new point and update cost

## Slide 70: RRT* : RRT + Path Improvements [It’s asymptotically optimal!]

## Slide 71: RRT* : RRT + Path Improvements [It’s asymptotically optimal!]

## Slide 72: RRT* : RRT + Path Improvements [It’s asymptotically optimal!]

## Slide 73: RRT* : RRT + Path Improvements [It’s asymptotically optimal!]

## Slide 74: RRT* : RRT + Path Improvements

## Slide 75: There are still some other considerations when using RRT* to plan
First, what about dynamics? How do we make sure our plans are still dynamically feasible if we are constantly changing the graph?

## Slide 76: There are still some other considerations when using RRT* to plan
First, what about dynamics? How do we make sure our plans are still dynamically feasible if we are constantly changing the graph?
Second, how should we sample? There is interesting work in strategies to get out of “traps” and through narrow passages.

## Slide 77: There are still some other considerations when using RRT* to plan
First, what about dynamics? How do we make sure our plans are still dynamically feasible if we are constantly changing the graph?
Second, how should we sample? There is interesting work in strategies to get out of “traps” and through narrow passages.
Also: when should we stop sampling? Not a clear-cut answer…

## Slide 78: Optimization for (local) trajectory planning with constraints
Task: travel from a start region to a goal region while (1) satisfying differential constraints and (2) avoiding obstacles.
Remember: the start and goal are in C-space; may include orientation.
We can run this to decide whether it is possible to “travel” in C-space through two points after an RRT* update.

## Slide 79: There are still some other considerations when using RRT* to plan
First, what about dynamics? How do we make sure our plans are still dynamically feasible if we are constantly changing the graph? Constraint-based optimization
Also, the trajectories we get are somewhat … jagged. Can we do anything about that?

## Slide 80: There are still some other considerations when using RRT* to plan

## Slide 81: Different Classes of Motion Planners
Sampling-based Planner
  PRM
  RRT (and its variants)
  DWA (the base local planner of move_base used in The BARN Challenge!)
Trajectory Optimization
  E-BAND (and its variants)
  CHOMP
  STOMP
Artificial Potential Field

## Slide 82: We have briefly addressed the 1st robot capability: motion control and planning
You already have everything you need for The BARN Challenge!
move_base
  Global Planner (Dijkstra’s, A*)
  Local Planner (DWA, E-BAND, TEB)
What do you want to do for your project?
  You can implement a new planner, e.g., PRM for global planning and RRT for local planning
  You can improve upon an existing motion planner
  You can develop your own motion planner (classical? Learning-based?)
We will move on to other robot capabilities next week!