## Slide 1: CS 685 Autonomous Robotics Human Robot Interaction
Prof. Xuesu Xiao
George Mason University
Slides Credits: Justin Hart

## Slide 2
There has been some form of interacting with machinery since the very first robots, including simple electro-mechanical devices that arguably may count from the turn of the 20th century
-Shultz & Goodrich, 2007

## Slide 3
Current Hot Topics
  Measuring human emotion & engagement
  Human-robot autonomous collaboration
  Physical human-robot interaction
  HRI as design
  Legibility of motion
Long-Standing Topics
  Generating and interpreting gaze attention
  Language & HRI
  Gesturing
  Back-channel communication
  Proxemics

## Slide 4: Kismet from MIT
https://www.youtube.com/watch?v=8KRZX5KL4fA

## Slide 5: Humanoids
Designed to function in a human-like way
Roughly human form

## Slide 6: Androids
Designed to look very human
Often (partially) tele-operated
  Geminoid
  Erica (https://www.youtube.com/watch?v=TyJ-xLj9SEE)

## Slide 7: The Uncanny Valley

## Slide 8: Physical HRI (pHRI)
Handovers
Shared Carrying
Exoskeletons
Collaborative assembly and manufacturing

## Slide 9: Often human interpretation of the stimulus is the important factor
Robots as evocative devices
Use of psychological methods to interpret results

## Slide 10: Experimental HRI & Psychology
User studies are a major driver of Human-Robot Interaction
Human-Robot Interaction is as much about understanding people well enough to write algorithms for robots as it is about the algorithms themselves

## Slide 11: Survey Metrics
Likert scale
  The robot was lifelike 1 – 2 – 3 – 4 – 5
Cognitive differences scale
  The robot was <not at all lifelike> – – <neither lifelike nor unlifelike> – – <very lifelike>

## Slide 12: Inter vs Intra Participant Design
Study conditions
  Group A – Control
  Group B – Experimental
  Group A – The robot plays a game with a participant
  Group B – The robot makes eye contact when it wants to influence the participant’s decisions in the game
Inter-participant
  Each participant sees exactly one experimental condition
Intra-participant
  Each participant sees every experimental condition
Why the difference?
  If the participant sees every condition, will it change the outcome?
  Can you get enough data?

## Slide 13: Statistical Tests
Null hypothesis
  The hypothesis that nothing significant is happening. The default. There is no difference between your conditions in terms of their effect on the variable that you are measuring.
t-tests & ANOVA (and its variants)
  Establish that two conditions are different from each other
    People like robots that smile more than ones that frown
    A robot in the same room as a person has more influence over that person’s behavior than a telepresent agent
Correlation tests (Pearson, Spearman)
  Establish that two values correlate to each other
    More automation is associated with higher employment
Statistical significance
  p – Probability value. The probability of obtaining test results at least as extreme as the observed results, assuming that the null hypothesis is correct.
    This is to say, how probable is it that your statistical test demonstrates nothing
  α – How small should p be to be considered “significant.”

## Slide 14: A Case Study: Evaluating Social Robot Navigation
14
Planning the most efficient, shortest length, minimal time plan?
Social compliance improves motion planning performance!
Performer-MPC
[XX et al., CoRL22]

## Slide 15: A Case Study: Evaluating Social Robot Navigation
15
Performer-MPC
[XX et al., CoRL22]
Blind Corner
Learning to anticipate Pedestrians
Pedestrian Obstruction
Learning to respect comfort distance

## Slide 16: A Case Study: Evaluating Social Robot Navigation
16
[P. L. XX et al., ICRA22WS]

## Slide 17: A Case Study: Adaptive Planner Parameter Learning from Non-Expert Human Interactions
Adaptive Planner Parameter Learning from Demonstration (APPLD)
  [XX et al., RA-L20]
Adaptive Planner Parameter Learning from Interventions (APPLI)
  [Wang et al., ICRA21]
Adaptive Planner Parameter Learning from Evaluative Feedback (APPLE)
  [Wang et al., RA-L21]
Adaptive Planner Parameter Learning from Reinforcement (APPLR)
  [Xu et al., ICRA21]
Cycle-of-Learning from APPL
  [Xiao et al., RAS22]

## Slide 18: Adaptive Planner Parameter Learning (APPL)
Robots need to face entirely different obstacle configurations.
Classical navigation systems require expert roboticists to fine-tune planner parameters.
max_vel_x: 0.5
min_vel_x: 0.1
max_vel_theta: 1.57
min_vel_theta: -1.57
vx_samples: 6
vtheta_samples: 20
occdist_scale: 0.1
pdist_scale: 0.75
gdist_scale: 1.0
Inflation_radius: 0.30
......

## Slide 19: Adaptive Planner Parameter Learning (APPL)
Inspiration: Most humans are not robotics experts, but they are navigation experts.
Teleoperated Demonstration
Corrective Interventions
Evaluative Feedback
Reinforcement Learning

## Slide 20: In Navigation Language…
[ROS move_base]

## Slide 21: In Learning Language…
[Gao et al., CoRL17, Pfeiffer et al., ICRA17, Chiang et al., RA-L19, Xiao et al., RA-L21]
[Xiao et al., RA-L20, Wang et al., ICRA21, Wang et al., RA-L21, Xu et al., ICRA21]

## Slide 22: APPL from Human Interactions [Xiao et al., RAS22]

## Slide 23: Adaptive Planner Parameter Learning from Demonstration (APPLD) [Xiao et al., RA-L20]
APPLD imposes an internal structure to the general parameter policy
Context Predictor
Parameter Library
State
Context
Param.

## Slide 24: Adaptive Planner Parameter Learning from Demonstration (APPLD) [Xiao et al., RA-L20]
Context Predictor:
2. Perform automatic segmentation (e.g., using CHAMP [Niekum et al. ICRA15])
1. Collect demonstration
3. Train online context predictor

## Slide 25: Adaptive Planner Parameter Learning from Demonstration (APPLD) [Xiao et al., RA-L20]
Parameter Library: For each context, use behavior cloning to construct each element of the parameter library
Behavioral Cloning: Learn parameters from a demonstration using supervised learning.
max_vel_x: 0.5
min_vel_x: 0.1
max_vel_theta: 1.57
min_vel_theta: -1.57
vx_samples: 6
vtheta_samples: 20
occdist_scale: 0.1
pdist_scale: 0.75
gdist_scale: 1.0
Inflation_radius: 0.30
......

## Slide 26: Adaptive Planner Parameter Learning from Demonstration (APPLD) [Xiao et al., RA-L20]

## Slide 27: Adaptive Planner Parameter Learning from Demonstration (APPLD) [Xiao et al., RA-L20]

## Slide 28: Adaptive Planner Parameter Learning from Demonstration (APPLD) [Xiao et al., RA-L20]

## Slide 29: APPL from Human Interactions [Xiao et al., RAS22]

## Slide 30: Adaptive Planner Parameter Learning from Interventions (APPLI) [Wang et al., ICRA21]
Robots do not behave suboptimally everywhere: Intervention when necessary
Ctx. Pred.
Param. Library
State
Context
Param.
Confident?
Y
N
Default Param.

## Slide 31: Adaptive Planner Parameter Learning from Interventions (APPLI) [Wang et al., ICRA21]
1. Collect (naturally segmented) interventions
3. Behavior clone parameters for each intervention
Context Predictor:
Parameter Library
2. Train context predictor with Evidential Deep Learning (EDL) [Sensoy et al. NeurIPS18]

## Slide 32: APPL from Human Interactions [Xiao et al., RAS]

## Slide 33: Adaptive Planner Parameter Learning from Evaluative Feedback (APPLE) [Wang et al., RA-L21]
Non-expert users may not be able to take control of the robot: Evaluative feedback
Feedback Predictor
Parameter Library
State
Best Feedback
Param.
Discrete APPLE

## Slide 34: Discrete Adaptive Planner Parameter Learning from Evaluative Feedback (APPLE) [Wang et al., RA-L21]
Feedback Predictor:
Existing Parameter Library (from default, manually tuned, APPLD, APPLI, etc.)
1. Collect feedback set
2. Train feedback predictor
3. Deploy parameter policy

## Slide 35: Adaptive Planner Parameter Learning from Evaluative Feedback (APPLE) [Wang et al., RA-L21]
Non-expert users may not be able to take control of the robot: Evaluative feedback
Policy Network
State
Parameters
Continuous APPLE

## Slide 36: Continuous Adaptive Planner Parameter Learning from Evaluative Feedback (APPLE) [Wang et al., RA-L21]
Policy Network:
Parameter Space instead of Parameter Library
Train in actor-critic style
Actor
Critic

## Slide 37: APPL from Human Interactions [Xiao et al., RAS22]

## Slide 38: Adaptive Planner Parameter Learning from Reinforcement (APPLR) [Xu et al., ICRA21]
What about no humans at all?
Policy Network
State
Parameters
APPLR
Reinforcement Learning
Benchmark Autonomous Robot Navigation (BARN) Dataset [Perille et al., SSRR21]

## Slide 39: Adaptive Planner Parameter Learning from Reinforcement (APPLR) [Xu et al., ICRA21]
Optimization Objective:
Reward Design:

## Slide 40: APPL from Human Interactions [Xiao et al., RAS22]

## Slide 41: Cycle-of-Learning from APPL [Xiao et al., RAS22]
[Xu et al., ICRA21]
[Wang et al., RA-L21]
[Xiao et al., RA-L20]
[Wang et al., ICRA21]

## Slide 42: References
Xiao, Xuesu, Bo Liu, Garrett Warnell, and Peter Stone. "Motion planning and control for mobile robot navigation using machine learning: a survey." Autonomous Robots (2022): 1-29.
Gao, Wei, David Hsu, Wee Sun Lee, Shengmei Shen, and Karthikk Subramanian. "Intention-net: Integrating planning and deep learning for goal-directed autonomous navigation." In Conference on Robot Learning, pp. 185-194. PMLR, 2017.
Pfeiffer, Mark, Michael Schaeuble, Juan Nieto, Roland Siegwart, and Cesar Cadena. "From perception to decision: A data-driven approach to end-to-end motion planning for autonomous ground robots." In 2017 ieee international conference on robotics and automation (icra), pp. 1527-1533. IEEE, 2017.
Chiang, Hao-Tien Lewis, Aleksandra Faust, Marek Fiser, and Anthony Francis. "Learning navigation behaviors end-to-end with autorl." IEEE Robotics and Automation Letters 4, no. 2 (2019): 2007-2014.
Xiao, Xuesu, Bo Liu, Garrett Warnell, and Peter Stone. "Toward agile maneuvers in highly constrained spaces: Learning from hallucination." IEEE Robotics and Automation Letters 6, no. 2 (2021): 1503-1510.
Xiao, Xuesu, Bo Liu, Garrett Warnell, Jonathan Fink, and Peter Stone. "APPLD: Adaptive planner parameter learning from demonstration." IEEE Robotics and Automation Letters 5, no. 3 (2020): 4541-4547.
Wang, Zizhao, Xuesu Xiao, Bo Liu, Garrett Warnell, and Peter Stone. "APPLI: Adaptive planner parameter learning from interventions." In 2021 IEEE International Conference on Robotics and Automation (ICRA), pp. 6079-6085. IEEE, 2021.
Wang, Zizhao, Xuesu Xiao, Garrett Warnell, and Peter Stone. "APPLE: Adaptive planner parameter learning from evaluative feedback." IEEE Robotics and Automation Letters 6, no. 4 (2021): 7744-7749.
Xu, Zifan, Gauraang Dhamankar, Anirudh Nair, Xuesu Xiao, Garrett Warnell, Bo Liu, Zizhao Wang, and Peter Stone. "APPLR: Adaptive planner parameter learning from reinforcement." In 2021 IEEE International Conference on Robotics and Automation (ICRA), pp. 6086-6092. IEEE, 2021.
Niekum, Scott, Sarah Osentoski, Christopher G. Atkeson, and Andrew G. Barto. "Online bayesian changepoint detection for articulated motion models." In 2015 IEEE International Conference on Robotics and Automation (ICRA), pp. 1468-1475. IEEE, 2015.
Sensoy, Murat, Lance Kaplan, and Melih Kandemir. "Evidential deep learning to quantify classification uncertainty." arXiv preprint arXiv:1806.01768 (2018).

## Slide 43: Final Project Presentation next week!
10-min presentation + 5-min Q&A (15-min per team)
  Reminder of what your project is about?
  What is your approach?
  What have you done?
  What are the results? Any thing learned?
  Project Demo! (Preferably live, at least recorded)
Remember the open-ended project is 40% of your final grade
  Devote 40% of the effort necessary for a 3-credit graduate-level course!
Final project report due in two weeks

## Slide 44: Course Evaluation
Please help fill in the course evaluation form at https://gmu.bluera.com/gmu/
Your feedback will be very helpful in improving future offerings of the course
Send the instructor a screenshot of proof of completion to get 5 points extra credit 